## Slide 1: Introduction to ISO 30500
Non-sewered sanitation systems – Prefabricated integrated treatment units – General safety and performance requirements for design and testing.
Notes: This presentation was prepared by TÜV SÜD.
Introduction

## Slide 2: ISO 30500 and ISO 31800 – Forward Looking Standards
Credits: Bill & Melinda Gates Foundation
ISO 31800 - Faecal sludge treatment units — Energy independent, prefabricated, community-scale, resource recovery units — Safety and performance requirements
ISO 30500 - Non-sewered sanitation systems — Prefabricated integrated treatment units — General safety and performance requirements for design and testing
+ Treatment
  “International Standards are key to the progression of new sanitation technology and developing an industry that saves lives”
- ISO Secretary-General Sergio Mujica

## Slide 3: Overview of ISO 30500
ISO 30500 Requirements
Human Health
Odour
Mechanical & HAZOP
Environmental
Noise
Air Emissions
Electrical & EMC
Frontend and backend
Backend only
Frontend only

## Slide 4: Scope of ISO 30500
Certification bodies – ISO 17076 accreditated
All laboratories – ISO 17025 accreditated
INPUT
FRONTEND(S)
BACKEND
COLLECTION/CONVEYANCE
OUTPUT
SAFE SOLID DISCHARGE OR
REUSE
SAFE LIQUID DISCHARGE OR
REUSE
AIR
EMISSION
ODOUR
NOISE
MECHANICAL
EMC
ELECTRICAL
Notes: The systems are generally separated by a frontend for the users. And a backend where the entire processing takes place.
Some of the main process output measurements are:
Solid and effluent discharge or reuse
Air emissions measurements
Odour
And Noise measurements

## Slide 5: ISO 30500 Certification Classes & Test Duration
Class
Class 1: Non-biological treatment processes one frontend – backend
Class 2: Biological treatment processes one frontend – multiple backends
Class 3: NSSSs – Biological treatment process multiple frontend – multiple backends
Class 4: Non-biological treatment processes multiple frontend – backend
Class 1 & 4 System
  Document Checks
  Controlled Laboratory Testing ≥ 22 days
  Field Testing for ≥ 30 days
Class 2 & 3 System
  Document Checks
  Controlled Laboratory Testing ≥ 22 days
  Field Testing for ≥ 5 months
No. of frontend | Class 1 & 2 | Class 3 & 4 | 
 | 1 frontend | 2-5 frontend | > 5 frontend
Superstructure requirement / Frontend testing | 1 | 2 | 3
Chart: Estimated % manhours commitment for complete certification
| Document check | Frontend testing | Controlled Laboratory Testing | Field Testing
Estimated % manhours commitment | 25 | 15 | 40 | 20
Notes: The Non-sewered sanitation systems can be classified into 4 different classes.

## Slide 6: ISO 30500 Overview
ISO 30500
Documentation Checks
Controlled Laboratory Testing
Field Verification of Performance
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Mechanical Requirements
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Loading Patterns
Loading Patterns
Notes: There are generally 3 main sections to the ISO30500. Document checks, controlled laboratory testing and the field verification.
The first requirement is for document checks and required tests to supplement missing documents.

## Slide 7
ISO 30500
Documentation Checks
Controlled Laboratory Testing
Field Verification of Performance
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Mechanical Requirements
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Loading Patterns
Loading Patterns
Normal (7.2.8.1)
Diarrhoea (A.3.8.10)
Stress (7.2.8.2)
Schedule
Notes: There are generally 3 main sections to the ISO30500. Document checks, controlled laboratory testing and the field verification.
The first requirement is for document checks and required tests to supplement missing documents.

## Slide 8: Controlled Laboratory Test Schedule
Human health and Environment Parameters
Odour Test
Noise and Air emissions
Legend
Notes: The schedule seen here is the schedule given in the standard. The first column depicts the kind of tests being done and the 2nd column is the corresponding type of loading pattern for the day. I’ve colour coded for better visibility.
There are a total of 5 days for human health and environmental testing for solid and effluent outputs.
4 days for odour tests, in which 1 day is done using the stress test. This is to test the consistency of results under different load conditions.
2 days are used for air emissions and noise. Similarly, stress is catered for 1 of the days to check the consistency of results.

## Slide 9: Normal Loading Pattern (7.2.8.1)
The loading of the system shall be performed as a percentage of daily load (kg/day of faeces, l/day of urine)
Capacity calculations indicated by the manufacturer
  uses per day (faecal uses/day and urine uses/day)
  the average amount of faeces (kg/use) and urine (l/use) per use
Loading shall be conducted at the corresponding timing:
  35 % from 6:00 to 9:00;
  25 % from 11:00 to 14:00;
  40 % from 17:00 to 20:00
Normal Loading Pattern | Example |  | 
(12 pax design) | ISO30500 (7.2.8) | Faeces (g) | Urine (l)
Total |  | 3000 | 15.6
6:00 – 9:00 | 35% | 1,050 | 5.46
11:00 – 14:00 | 25% | 750 | 3.90
17:00 – 20:00 | 40% | 1,200 | 6.24
Notes: The normal loading pattern is derived from the capacity calculations indicated by the manufacturer. Provision by the manufacturer, the number of uses per day and assumption of amount per use is required. The loading timing are spread across 6 am to 8 pm to simulate closely to real case scenarios.

## Slide 10: Stress (7.2.8.2)
Sanitation system is loaded with treatment capacity (TC) + “Sn”, where Sn is 80% of the difference between maximum capacity and treatment capacity. [Sn = 80% x ( Max – TC)]
Loading shall be conducted at the corresponding timing:
  35 % from 6:00 to 9:00;
  25 % from 11:00 to 14:00;
  40 % from 17:00 to 20:00
Example
Treatment capacity = 12 pax
Max capacity = 15 pax
Sn = (15 -12) x 80% = 2.4 pax
Stress loading = 12 + 2.4 = 14.4 pax
Normal Loading Pattern | Example |  | 
(14.4 pax design) | ISO30500 (7.2.8) | Faeces (g) | Urine (l)
Design |  | 3000 | 15.6
Max |  | 3750 | 19.5
Stress |  | 3600 | 18.7
6:00 – 9:00 | 35% | 1,260 | 6.6
11:00 – 14:00 | 25% | 900 | 4.7
17:00 – 20:00 | 40% | 1,440 | 7.5
Notes: For the stress test, the maximum capacity is required from the manufacturer to calculate the stress loading. The loading times are similar to the normal loading pattern.

## Slide 11: Diarrhoea (A.3.8.10)
For the diarrhoea test days, 50 % of the normal faeces loading shall be ‘diarrhoea input’ instead of solid faeces.
Half of this load is to be as normal faecal load (solid faeces), the other half diluted as diarrhoea input.
Combine fresh faeces with water at a ratio of
  2 L of water : 1 kg of fresh faeces.
Normal Loading Pattern | Example |  |  | 
 |  |  | Diarrhoea | 
(12 pax design) | ISO30500 (7.2.8) | Faeces (g) | Faeces (g) | Water (l)
Total |  | 1500 | 1500 | 3
6:00 – 9:00 | 35% | 525 | 525 | 1.1
11:00 – 14:00 | 25% | 375 | 375 | 0.7
17:00 – 20:00 | 40% | 600 | 600 | 1.2
Notes: For the diarrhoea input, we take 50% of the faeces and convert them into diarrhoea input to simulate real case scenario. The mixture to simulate diarrhoea is 2 litres of water for every 1 kg of faeces.
The target dry matter content of the diarrhoea input should be between 3 and 10%.
For this testing, the assumption is that each diarrhoea user produces 1.2 l of diarrhoea per day
There is no intent or need to be very precise about the dry matter content of the simulated diarrhoea sample, and thus a twofold dilution by mass of fresh healthy faeces shall be used.

## Slide 12
Frontend Requirements
Evacuation Performance (6.4)
Integrity against external impacts (6.5)
Slip, trip and falling (6.6)
Tightness Test (A.3.1)
Evacuation Mechanism (A.3.3)
Visibility of Faeces (6.3)
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Frontend Requirements
Environmental Parameters
Notes: Mechanical tests are mainly focused on the frontend and frontend area (except tightness test A3.1). These tests are not indicated in the schedule but is to be tested prior to commencing.
Water supply/ Pipework
Container Water test
Container Air (pressure)
Container Air (vacuum)

## Slide 13
Environmental Parameters
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Frontend Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Environmental Parameters
TSS
BOD
Total Nitrogen
Total Phosphorus
pH
Frontend Requirements
COD
Colour
Notes: Mechanical tests are mainly focused on the frontend and frontend area (except tightness test A3.1). These tests are not indicated in the schedule but is to be tested prior to commencing.
Water supply/ Pipework
Container Water test
Container Air (pressure)
Container Air (vacuum)

## Slide 14: Environmental Parameters Threshold
Public Exposure
Controlled Area
Notes: For areas with unrestricted access with public exposure, the thresholds are more stringent. Compared to urban reuse where public exposure to the reclaimed water is controlled.
For the load reduction of nutrients (total nitrogen & total phosphorus), the initial input samples have to be tested for comparison.
Unrestricted urban reuse involves the use of reclaimed water where public exposure is likely in the reuse application, thereby requiring a high degree of treatment. In general, all states that specify a treatment process require a minimum of secondary treatment and disinfection prior to unrestricted urban reuse.
Restricted urban reuse involves the use of reclaimed water where public exposure to the reclaimed water is controlled; therefore, treatment requirements may not be as strict as those for unrestricted urban reuse.

## Slide 15
Environmental Parameters
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Frontend Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Environmental Parameters
TSS
BOD
Total Nitrogen
Total Phosphorus
pH
Frontend Requirements
COD
Colour
Notes: Mechanical tests are mainly focused on the frontend and frontend area (except tightness test A3.1). These tests are not indicated in the schedule but is to be tested prior to commencing.
Water supply/ Pipework
Container Water test
Container Air (pressure)
Container Air (vacuum)

## Slide 16
Environmental Parameters
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Frontend Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Bacteria
Helminth
Protozoa
Virus
Human Health Parameters
Environmental Parameters
Notes: Mechanical tests are mainly focused on the frontend and frontend area (except tightness test A3.1). These tests are not indicated in the schedule but is to be tested prior to commencing.
Water supply/ Pipework
Container Water test
Container Air (pressure)
Container Air (vacuum)

## Slide 17: Human Health Parameters Spiking
Input
Output
NSSS
Spike
1
S1
2
S2
3
Spiking values
LRV = -
2
3
Threshold
Requirements to fulfill human health parameters
Thresholds and log reduction values requirements.
Notes: To meet the log reduction value, the initial input have to meet the minimum required concentration shown. To meet this concentration, spiking will need to be done during the normal loading pattern. And the frequency of the spike and testing is dependent on the manufacturers process. Is it a batch process, continuous or even periodic liquid discharge system.

## Slide 18: Microbial Testing
Microbe spiking
Microbe testing (Sample Taking)
TÜV SÜD Sustainable Sanitation Services| INTRODUCTION TO ISO 30500

## Slide 19
Environmental Parameters
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Frontend Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Bacteria
Helminth
Protozoa
Virus
Human Health Parameters
Air Emissions Parameters

## Slide 20
Environmental Parameters
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Frontend Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Indoor
Stack
NOx
H2S
PM2.5
SO2
VOC
NH3
Air Emissions Parameters
Human Health Parameters
CO2
CO

## Slide 21: Air Emissions - Indoor
Thresholds
Recommended Methods
Sampling Methods and Location
About 1 to 1.5 m from the ground above the squat or seat pan
Superstructure door to remain closed during entire sampling
Atmospheric air sampling pump
Notes: And the thresholds for the parameters are based on a 1 hour average sampling time. Except the H2S parameter which is measured at 30 mins average. The recommended test methods are provided in the standard as well. Please note that for air emissions testing methods, equivalent national standards are acceptable as well.

## Slide 22: Air Emissions Testing Indoor

## Slide 23
Indoor
Stack
CO
NOx
H2S
PM2.5
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
CO2
VOC
NH3
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Air Emissions Parameters
CO2
Notes: The parameters tested for the frontend are as shown.

## Slide 24
Indoor
Stack
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
NOx
H2S
PM2.5
O2
Moisture Content
CO
VOC
NH3
SO2
PAH
Vol. Flow
Air Emissions Parameters

## Slide 25: Air Emissions - Stack
Thresholds
Recommended Methods
Sampling Methods and Location
Most significant sources of air pollutants within the NSSS
External gas vent/Stack as outlined in EPA Method 1A
2D
8D
8D
10D
Sampling Point
Velocity and Temp. Measurement
EPA Method 1A
Notes: For the stack emissions, the parameters are all based on 1 hour averages with concentrations normalised to ambient conditions. Similarly, equivalent national standards are acceptable as well.

## Slide 26
Indoor
Stack
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
NOx
H2S
PM2.5
O2
Moisture Content
CO
VOC
NH3
SO2
PAH
Vol. Flow
Air Emissions Parameters
Acoustics Parameters

## Slide 27
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Acoustics Parameters
Within Superstructure
External
Air Emissions Parameters

## Slide 28: Acoustics Parameters (Internal)
Within superstructure / Frontend
For sanitation system that include a superstructure as part of the manufactured product, noise shall be measured within the superstructure at a single measurement point.
The measurement point shall be centred above the squatting or seat pan of the frontend at a height of 1,20 +/- 0,05 m from the ground.
Requirements: ≤ 60 dBA (average) & ≤ 85 dBA (max) across 24hrs
1.2 m
Notes: For the frontend, the requirement is a single point measurement above the squat or seat pan of 1.2m.
For the backend as per the example, measurement points are 1m outward, 1.2m height and 1m apart from each measurement point. The measurement point shall be determined relative to the smallest imaginary rectangular parallelepiped.
Measurement points nearest to the corners are discarded.

## Slide 29: Acoustics Parameters (External)
External / Backend
The measurement points shall be positioned on the surface of a measurement parallelepiped whose planes are each 1 m outward (relative to the system) from those of the reference parallelepiped.
Requirements: ≤ 60 dBA (average) & ≤ 85 dBA (max) across 24hrs
External / Backend Measurement
NSSS
NSSS
= MEASUREMENT POINTS
W
L
L/2
W/2
1m
1.2m
REFERENCE PARALLELEPIPED
= KEY MEASUREMENT POINT
= POINTS <1m NEAREST TO THE CORNERS TO BE DISCARDED
L = LENGTH
W = WIDTH
1m
1m
<1m
1m
1m
1m
1m
1m
1m
1m
1m
<1m
<1m
1.2m
1m
MEASUREMENT PARALLELEPIPED
Notes: For the frontend, the requirement is a single point measurement above the squat or seat pan of 1.2m.
For the backend as per the example, measurement points are 1m outward, 1.2m height and 1m apart from each measurement point. The measurement point shall be determined relative to the smallest imaginary rectangular parallelepiped.
Measurement points nearest to the corners are discarded.

## Slide 30: Noise Emissions Testing Indoor and outdoor

## Slide 31
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Acoustics Parameters
Within Superstructure
External
Odour Requirements

## Slide 32
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Odour Requirements
Acoustics Parameters
Within Superstructure (Frontend)
External (Vicinity)

## Slide 33: Odour – Requirements
Sample Odour Assessment Report Sheet
1. Test Frequency
2. Threshold
Per test
Instruct the panelists to inhale the surrounding air and smell its odour at 10 s intervals, for total duration of 3 min per test
Notes: Location of test is at the frontend.
A record is done for every 10s for total of 3 minutes per event.
For a typical odour test day,
4 faecal events
2 urinary events
2 events when process is expected to release the most odours
2 randomly during the test
At the end of the test, the results have to be tabulated and meet the maximum threshold percentage given.
For the indoor testing, systems with 2 – 5 front ends is required to minimally test for 2 frontends. Systems with more than 5 frontends will need to test for minimally 3 frontends.

## Slide 34: Odour Emissions Testing
Odour Assessment by panelist
Simulant Preparations
Panelist Odour Screening

## Slide 35
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Odour Requirements
Electrical Requirements
Within Superstructure (Frontend)
External (Vicinity)

## Slide 36
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Electrical Requirements
Odour Requirements
Energy discharge (A.3.8.4)
Control System (A.3.2)
1. Disconnect and discharge remaining energy.
2. Record energy remaining in system.
3. If backup energy is present, check and record capacity of backup source.
Tested prior to test sequence.
To develop test plan to test each control function independently
Field Testing Guidelines

## Slide 37
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Electrical Requirements
Field Testing Guidelines
Class 1 & 4
Class 2 & 3
Test Duration 30 days
Human Health & Environmental Testing Weekly
Test Duration 5 Months
Environmental Testing Weekly
Human Health Testing Monthly
Class
Class 1: Non-biological treatment processes one frontend – backend
Class 2: Biological treatment processes one frontend – multiple backends
Class 3: NSSSs – Biological treatment process multiple frontend – multiple backends
Class 4: Non-biological treatment processes multiple frontend – backend

## Slide 38: Field Testing Guidelines
 |  | Month 1 |  |  |  | Month 2 |  |  |  | Month 3 |  |  |  | Month 4 |  |  |  | Month 5 |  |  |  | 
Week | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 25
Class 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Environmental | D | W | W | W | W | C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Human Health |  | W | W | W | W | C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Class 2 & 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Environmental | D | W | W | W | W | W | W | W | W | W | W | W | W | W | W | W | W | W | W | W | W | C
Human Health |  | M |  |  |  | M |  |  |  | M |  |  |  | M |  |  |  | M |  |  |  | C
Legends
B = Inlet Baseline study (daily). Total N & P only
D = Daily sampling
W = Weekly sampling
M = Monthly sampling
C = Complete

## Slide 39
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Electrical Requirements
Field Testing Guidelines
Class 1 & 4
Class 2 & 3
Test Duration 30 days
Human Health & Environmental Testing Weekly
Test Duration 5 Months
Environmental Testing Weekly
Human Health Testing Monthly
Environmental Parameters (Field)
Class
Class 1: Non-biological treatment processes one frontend – backend
Class 2: Biological treatment processes one frontend – multiple backends
Class 3: NSSSs – Biological treatment process multiple frontend – multiple backends
Class 4: Non-biological treatment processes multiple frontend – backend

## Slide 40
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Field Testing Guidelines
TSS
BOD
Total Nitrogen
Total Phosphorus
pH
Input samples to be collected and analysed daily for a period of 1 week to collect total nitrogen and total phosphorus baseline values.
Environmental Parameters (Field)
Human Health Parameters (Field)
COD
Colour
75% Pass Requirement

## Slide 41
Documentation Checks
Controlled Laboratory Testing
ISO 30500
General Technical Information
Process Design Safety
Material Safety
General Safety
User Interface Experience
Maintenance Design
Mech. & Elec. Safety
Loading Patterns
Environmental Parameters
Human Health Parameters
Air Emissions Parameters
Acoustics Parameters
Odour Requirements
Sustainability
Electrical Requirements
Mechanical Requirements
Field Verification of Performance
Environmental Parameters
Human Health Parameters
Field Testing Guidelines
Human Health Parameters (Field)
Environmental Parameters (Field)
100% Pass Requirement
Bacteria
Protozoa
Virus
Human enteric Protozoa validates treatment efficiency for human enteric Helminths

## Slide 42: Frequent Asked Questions
What is the cost of certification of one unit?
What is the breakdown of cost for the different testing?
Is it still possible to make any changes to the document?

## Slide 43: Thank You!
Coimbatore, India
ISO 30500 Validation Testing
Durban, South Africa
ISO 30500 Validation Testing
Kathmandu, Nepal
ISO 30500 Project Committee
Yixing, China
ISO 30500 Preliminary Testing
Dakar, Senegal
Laboratories Kickoff Meeting